## Slide 1: Introduction
Kellie Koedel
MH Companies

## Slide 2: Agenda
FHWA ruling – motivation for change
Review AASHTO
  What’s new for 2015!
Why Fatigue Categories Matter
  Importance Factor
Examples
Don’t let your engineered drawings get copied
How to write a spec
  Valmont only for government
Cost difference current, 2015 FC1, 2015 FC2 mitigator

## Slide 4
AASHTO
Denver: 2001, FC2 no galloping. 100MPH

## Slide 5: FHWA Final Ruling:
Department of Transportation, Federal Highway Administration 23 CFR Part 625
  Final Ruling - Required design standards on Federal-aid highway projects…..AASHTO LTS6 - 2013
  Effective Date for New Projects after November 12, 2015
  The rule is not retroactive to current projects.

## Slide 6: The AASHTO Evolution:
Standard Specifications for Structural Supports for Highway Signs, Luminaires and Traffic Signals
1975
Standard Specifications for Structural Supports for Highway Signs, Luminaires and Traffic Signals
1984
Standard Specifications for Structural Supports for Highway Signs, Luminaires and Traffic Signals
1994
1975
1984
1994
2001
2001 – Changed from Fastest Mile to 3 Second Gust Wind Loading
2001 - Fatigue Design Introduced (Section 11)
2013 – Minimum Required design standards on Federal-aid highway projects
2015 – Load Resistance Design Factor (ultimate wind) Introduced
2009
2015
2013

## Slide 7: Fatigue Category - AASHTO 2001:
Choosing a Fatigue Category (AASHTO 2001 C11.6):
  Fatigue Category I: Most Stringent
    High Hazard in the event of failure and should be designed to resist rarely occurring wind loading and vibration phenomena.
    The most Critical cantilevered support structures.
    Large sign structures, Variable message sign (VMS), Traffic Structures with long arms, High level lighting structures in excess of 98 feet that are installed on highways where the vehicle speed is such that the consequences of excessive deflection or collision with a fallen structure is intolerable.
  Fatigue Category III: Least Stringent
    Structures less likely to experience the full limit state wind loads associated with Category I.
  Fatigue Category II:
    Structures less likely to experience the full limit state wind loads associated with Category I.

## Slide 8: Fatigue Category - AASHTO 2013 & 2015:
Choosing a Fatigue Category (AASHTO 2013/2015 C11.6):
  Fatigue Category I: Most Stringent
    AASHTO Recommends that all Structures without effective mitigation devices on roadways with a speed limit in excess of 35 mph and ADT exceeding 10,000, or ADTT exceeding 1,000 be designed to Fatigue Category I.
    Cantilevered sign structures without mitigation devices with a span in excess of 50 feet be designed to Fatigue Category I.
    Large sign structures, both cantilevered and non-cantilevered, including variable message signs, without mitigation devices be designed to Fatigue Category I.
    Structures without mitigation devices located in an area that is known to have wind conditions that are conducive to vibrations be designed to Fatigue Category I.
    Structures classified as Category I should be designed to resist rarely occurring wind loading and vibration phenomena.
  Fatigue Category III: Least Stringent
    Structures located on roads with speed limits of 35 mph or less.
    Structures that are located such that a failure will not affect traffic.
  Fatigue Category II:
    All structures not explicitly meeting the Category I or Category III criteria.
Note:
Quantifies FC1
References
mitigation device
*kk - road design avg is 1900 per lane per hour

## Slide 9: 2013 vs 2015
2013 uses the old design method and wind maps. Will be more familiar to traffic engineers
2015 uses the new LRFD (Load Resistance Design Factor) and Ultimate wind
  Newer AASHTOs coming will be based on LRFD so 2015 will be more current longer

## Slide 10: 55’ Mast Arm Example
Fatigue Category 2 justified with use of mitigation device
 | Pole |  |  | Arm |  |  |  |  |  | 
 | Diameter (in.) | Thickness (in.) | Length (ft.) | Diameter (in.) | Thickness (in.) | Length (ft.) | Total Weight (shafts, baseplate flanges) | % Weight Change |  | 
2001 Design | 15 | 0.3125 | 39 | 14.75 | 0.3125 | 55 | 3,792 |  |  | 
2013 // FC 1 // Gal | 19.5 | 0.3125 | 39 | 22 | 0.5 | 55 | 7,449 | 96% |  | 
2013 // FC 2 // Gal | 19.5 | 0.3125 | 39 | 18 | 0.3125 | 55 | 5,071 | 34% |  | 
2013 // FC 2 // with TR1 for Gal | 16 | 0.3125 | 39 | 14.5 | 0.3125 | 55 | 3,457 | -9% |  | 
 | Baseplate |  |  |  |  | Anchor Bolts | 
 | Square (in.) | Bolt Circle (in.) | Thickness (in.) | Center Hole Diameter (in.) | Baseplate Weight (lbs) | Diameter (in.) | Quantity
2001 Design | 20 | 20 | 1.75 | 8 | 180 | 2 | 4
2013 // FC 1 // Gal | 30.5 x 27.25 | 24.88 | 3 | 10 | 633 | 2.25 | 6
2013 // FC 2 // Gal | 26.5 | 26.5 | 2 | 10.75 | 350 | 2.25 | 4
2013 // FC 2 // with TR1 for Gal | 22.5 | 22.5 | 2 | 13 | 210 | 2 | 4

## Slide 11: Fatigue Loads:
Galloping Loads (Section 11.7.1.1)
Truck-Induce Loads (Section 11.7.1.3)
Galloping and Truck-Induced Loads Recommended Deflection Requirements (Section 11.8)
High Mast (Natural Wind and Vortex Shedding Combination) (Section 11.7.2)
Vortex Shedding
Natural Wind Gusts (Section 11.7.1.2)

## Slide 12: Galloping Loads:
Galloping (AASHTO 2013/2015 11.7.1.1):
  All Category I Structures should be designed to resist Galloping Forces, unless an effective mitigation device is installed. (C11.6)
  No Galloping Loads when an effective mitigation device is installed.
  For Traffic Signal Poles, the Owner may choose to install an effective mitigation device when a structure displays a galloping problem and it should be installed as quickly as possible.
  Importance Factors, IF
    Category I: IF = 1.0
    Category II: IF = 0.65 Traffic or 0.70 Sign
    Category III: IF = 0.30 Traffic or 0.40 Sign
PG= 21(IF)
FG= PG(A)
Where:
PG = Vertical shear pressure range
IF = Importance Factor
FG = Galloping Force Load
A = Frontal Project Area of Signs and Signals

## Slide 13: Galloping Loads:
Pennsylvania Mast Arm

## Slide 14: Truck-Induced Loads:
Truck-Induced (AASHTO 2013/2015 11.7.1.3):
  Applies to all Cantilevered and non-cantilevered sign and traffic signal structures.
  All Category I Structures should be designed to resist rarely occurring vibration phenomena. (C11.6)
  The truck-induced gust loading shall be excluded, unless required by the Owner for traffic signal structures.
Importance Factors, IF
  Category I: IF = 1.0
  Category II: IF = 0.85 Traffic or 0.90 Sign
  Category III: IF = 0.70 Traffic or 0.80 Sign
PTG= 18.8(Cd)(IF)
FTG= PTG(A)
Where:
PTG = Static truck gust pressure range (12 foot worst case range)
IF = Importance Factor
Cd = Drag Coefficient based on 65mph vehicle speed
FTG = Truck gust Force Load
A = Bottom Project Area of Signs and Signals and Arm
*accounts for 1 12’ section

## Slide 15: Natural Wind Gusts:
Natural Wind Gust (AASHTO 2013/2015 11.7.1.2):
  Cantilevered and non-cantilevered over head sign and traffic signal supports shall be designed to resist Natural Wind Gust Loads.
  No Natural Gust Loading exclusion when using a mitigation device.
PNG = 5.2(Cd)(IF)
FNG = PTG(A)
Importance Factors, IF
  Category I: IF = 1.0
  Category II: IF = 0.80 Traffic or 0.85 Sign
  Category III: IF = 0.55 Traffic or 0.70 Sign
Where:
PNG = Natural wind gust pressure range
IF = Importance Factor
Cd = Drag Coefficient based on 11.2 mph wind speed
FNG = Natural wind gust force load
A = Frontal Project Area of Signs and Signals and Arm & Pole

## Slide 16: The Valmont Solution:

## Slide 17: Testing at UCONN
Free Vibration Test (50’ Lg Arm w/125 lbs. Mass - 0.99 Hz)
Undampened
Dampened
Slender 50 foot mast arm

## Slide 18: Testing at UCONN
Forced Vibration Test (50’ Lg Arm w/125 lbs. Mass - 0.99 Hz)
Undampened
Dampened
Slender 50 foot mast arm

## Slide 19: 55’ Mast Arm Example
Fatigue Category 2 justified with use of mitigation device
 | Pole |  |  | Arm |  |  |  |  |  | 
 | Diameter (in.) | Thickness (in.) | Length (ft.) | Diameter (in.) | Thickness (in.) | Length (ft.) | Total Weight (shafts, baseplate flanges) | % Weight Change |  | 
2001 Design | 15 | 0.3125 | 39 | 14.75 | 0.3125 | 55 | 3,792 |  |  | 
2013 // FC 1 // Gal | 19.5 | 0.3125 | 39 | 22 | 0.5 | 55 | 7,449 | 96% |  | 
2013 // FC 2 // Gal | 19.5 | 0.3125 | 39 | 18 | 0.3125 | 55 | 5,071 | 34% |  | 
2013 // FC 2 // with TR1 for Gal | 16 | 0.3125 | 39 | 14.5 | 0.3125 | 55 | 3,457 | -9% |  | 
 | Baseplate |  |  |  |  | Anchor Bolts | 
 | Square (in.) | Bolt Circle (in.) | Thickness (in.) | Center Hole Diameter (in.) | Baseplate Weight (lbs) | Diameter (in.) | Quantity
2001 Design | 20 | 20 | 1.75 | 8 | 180 | 2 | 4
2013 // FC 1 // Gal | 30.5 x 27.25 | 24.88 | 3 | 10 | 633 | 2.25 | 6
2013 // FC 2 // Gal | 26.5 | 26.5 | 2 | 10.75 | 350 | 2.25 | 4
2013 // FC 2 // with TR1 for Gal | 22.5 | 22.5 | 2 | 13 | 210 | 2 | 4

## Slide 20: 30’
VALMONT INDUSTRIES |  |  |  |  |  |  |  |  |  |  |  |  | 
AASHTO 100mph FC1 & FC2 Comparisons |  |  |  |  |  |  |  | 1/29/2018 |  |  |  |  | 
30' MAST ARM | 1-piece |  |  |  |  |  |  |  |  |  |  |  | 
 | Fatigue Category | Galloping Included | Truck Gust Included (45 MPH) | Wind Load Included | Pole Base Size & thickness | # anchor bolt | anchor bolt size | mast arm base and thickness | arm connection simplex size | # connection bolt | connection bolt size | weight (lbs) | weight difference
2001 Current Design | 2 | NO | YES | YES | 15.5 (.2188) | 4 | 2 | 12 (.2092) | 21.75 sq | 4 | 1.5 | 2013 | 
2013 AASHTO FC1 Galloping | 1 | YES | YES | YES | 16.5 (.25) | 4 | 2 | 14.9 (.25) | 22.25 sq | 4 | 1.5 | 2685 | 33.4%
2013 AASHTO FC2 galloping | 2 | YES | YES | YES | 15 (.1875) | 4 | 2 | 12.5 (.2391) | 20.25 sq | 4 | 1.25 | 1959 | -2.7%
2013 AASHTO FC2 TR1 For galloping | 2 | DEFAULT | DEFAULT | YES | 15 (.1875) | 4 | 2 | 10 (.1793) | 20.25 sq | 4 | 1.25 | 1618 | -19.6%
 |  |  |  |  |  |  |  |  | *MUST MEET HANDHOLE CRITERIA FOR AASHTO 2013 |  |  |  | 
Current: 2001, FC2 no galloping

## Slide 21: 50’
50' MAST ARM | 2-piece |  |  |  |  |  |  |  |  |  |  | wgt | wgt
 | Fatigue Category | Galloping included | Truck Gust Included | Wind Load Included | Pole Base Size & thickness | # anchor bolt | anchor bolt size | mast arm base and thickness | arm connection simplex size | # connection bolt | connection bolt size | weight (lbs) | weight difference
2001 Current Design | 2 | NO | YES | YES | 17 (.2188) | 4 | 2 | 15 (.25) | 23.25 sq | 4 | 1.5 | 2933 | 
2013 AASHTO FC1 Galloping | 1 | YES | YES | YES | 21 (.375) | 4 | 2 | 18.5 (.3125) | 29.50 sq | 8 | 1.5 | 5270 | 79.7%
2013 AASHTO FC2 galloping | 2 | YES | YES | YES | 18 (.25) | 4 | 2 | 16.5 (.25) | 23.75 sq | 4 | 1.25 | 3442 | 17.4%
2013 AASHTO FC2 TR1 For galloping | 2 | DEFAULT | DEFAULT | YES | 17 (.2188) | 4 | 2 | 15 (.25) | 23.25 sq | 4 | 1.25 | 2933 | 0.0%
 |  |  |  |  |  |  |  |  | *MUST MEET HANDHOLE CRITERIA FOR AASHTO 2013 |  |  |  | 
Used Current DB00714 Standard Loadings |  |  |  |  |  |  |  |  |  |  |  |  | 
X

## Slide 22: Don’t hand out too much info
Material cost difference
basis
50% higher
10% higher

## Slide 23: Drawings
New TK drawing
Take out the engineering secrets but keep the pertinent info the customer needs.
Spec in stamped letter will work for approval
  Conversation to explain how our industry works and trade secrets

## Slide 24: DB Drawing

## Slide 25: TK drawing (same drawing #)

## Slide 26: How to Write a Spec
Anyone can submit a 2015 compliant design.
  We are the only ones with a mitigation device
Have a list of currently approved devices
Mitigation devices must have prior approval from city
Liability that all parts come from one manufacturer

## Slide 27: Written Spec
**if handing out stamped drawings mark them proprietary

## Slide 28: Written Spec

## Slide 29: THANK YOU!
valmontstructures.com
Kellie Koedel
MH Companies
720-989-0066